## Slide 1: BT209 Bioreaction Engineering
10/03/2022

## Slide 2
When a material reacts away (AR) by any nth order rate (n > 0) in a batch reactor, its rate of disappearance is rapid at the start when the concentration of reactant is high. This rate then slows progressively as reactant is consumed.
Reactions with such rate-concentration curves lead to interesting optimization problems
Autocatalytic reaction and reactor
nth order reaction (n>0) AR
Autocatalytic reaction
In an autocatalytic reaction, however, the rate at the start is low because little product is present; it increases to a maximum as product is formed and then drops again to a low value as reactant is consumed. Figure 6.18 shows a typical situation.

## Slide 3
For any particular rate-concentration curve a comparison of areas in Fig. will show which reactor is superior (which requires a smaller volume) for a given job.
At low conversion the mixed reactor is superior to the plug flow reactor.
At high enough conversions the plug flow reactor is superior.
Plug Flow Versus Mixed Flow Reactor, No Recycle
For autocatalytic reactions mixed flow is more efficient at low conversions, plug flow is more efficient at high conversions.

## Slide 4
These findings differ from ordinary nth-order reactions (n > 0) where the plug flow reactor is always more efficient than the mixed flow reactor.
In addition, we should note that a plug flow reactor will not operate at all with a feed of pure reactant. In such a situation the feed must be continually primed with product, an ideal opportunity for using a recycle reactor.
Using optimization problems we can find the optimum recycle ratio which gives the minimum reactor volume or minimum space time
Cont..
xAf
FAf
CAf
vf
xA0
FA0
CA0
vo

## Slide 5
The most important examples of autocatalytic reactions are the broad class of fermentation
reactions which result from the reaction of microorganism on an organic feed.
When they can be treated as single reactions, the methods of this chapter can be applied
directly.
Occurrence of Autocatalytic Reactions
S+ Cell  More cell

## Slide 6
When material is to be processed to some fixed final conversion XAf in a recycle reactor, reflection suggests that there must be a particular recycle ratio (R) which is optimum in that it minimizes the reactor volume or space-time.
Optimum Recycle Operations
xAf
FAf
CAf
vf
xA3
FA3
CA3
v3
xA2
FA2
CA2
v2
xA1 (xAi)
FA1
CA1
v1
xA0
FA0
CA0
vo

## Slide 7
xAf
FAf
CAf
vf
xA3
FA3
CA3
v3
xA2
FA2
CA2
v2
xA1 (xAi)
FA1
CA1
v1
xA0
FA0
CA0
vo
FA
FA+dFA
dV
The optimum recycle ratio is found by differentiating Eq. with respect to R and setting to zero, thus
Cont.

## Slide 8
for
Cont.

## Slide 9
In words, the optimum recycle ratio introduces to the reactor a feed whose 1/(-rA) value (KL in Fig.) equals the average 1/(-rA) value in the reactor as a whole (PQ in Fig.).
xAf
FAf
CAf
vf
xA3
FA3
CA3
v3
xA2
FA2
CA2
v2
xA1 (xAi)
FA1
CA1
v1
xA0
FA0
CA0
vo
Cont.

## Slide 10
For autocatalytic reactions
In general, for a rate-concentration curve as shown in Fig one should always try to reach point M in one step (using mixed flow in a single reactor), then follow with plug flow or as close to plug flow as possible. This procedure is shown as the shaded area in Fig.
Reactor combination for autocatalytic reaction with out recycle
XA0=0
XAf
XAopt
MFR
PFR
XAopt
XAf
XA0=0